## Slide 1: How to use this supplement (delete before the talk)
Slides 7–17 are Sterling's EMC 2026 originals — animations intact. Copy with “Keep Source Formatting.”
Every video on these slides is a real embedded clip; click to play, no internet needed.
Working slides (this one, and the last two) are planning aids, not talk slides.
Notes: Not a talk slide. Built by presentation/build_supplement_deck.py.

## Slide 2: A tensegrity lander can hit the ground at highway speed, bounce, and still get up.
NASA Super Ball Bot / NIAC Titan mission concept — 20 s excerpt. Credit: NASA.
Notes: Open here. Play the clip silently, say nothing for the first five seconds. Then the scope line: a printed PLA-TPU T3 prism is our proxy for developing the workflow, not flight hardware.

## Slide 3: Tensegrity: rigid struts that never touch each other, held apart by cables in pure tension.
Steve Mould, “Tensegrity Explained” (youtube.com/watch?v=0onncd0_0-o) — 18 s excerpt, used with on-screen credit.
Notes: The 2D teaching model is the fastest way to make the mechanism obvious: push it, it springs back, nothing is glued. Say out loud that load paths are tension-only in the cables.

## Slide 4: Crushable honeycomb absorbs one impact; a tensegrity structure survives drop after drop.
SUPERball v2 3.4 m drop — IEEE Spectrum / NASA Ames (youtube.com/watch?v=hkzeE6BVNIk), 10 s excerpt.
Notes: This is the reusability argument Sterling asked for: the same hardware takes the next drop. It is also why our own campaign can re-test a specimen instead of consuming it.

## Slide 5: Tensegrity impact structures already exist — every one of them was designed and assembled by hand.
NASA SUPERball v2 — hand-built, one design, no optimization loop
Davami 2025 — printed tensegrity, characterized but not optimized
Gu & Dotov — tensegrity crutch tip: the application pull is real
TODO before freeze: verify citations against manuscript/references.bib.
Notes: Three names, ten seconds. The point is not a literature review; it is that the design step is still manual everywhere.

## Slide 6: Nobody closes the loop: print the structure, drop it, and let the measured data choose the next design.
TODAY
Hand-tuned geometry
Simulation, rarely validated
One-off demonstrations
THIS WORK
The drop test is the objective
Trade-offs learned from shock data
One printer, one tower, one loop
Notes: This is the motivation-to-gap transition. Do not read the columns; point left, point right, move on.

## Slide 7: Bayesian optimization is a machine learning technique that works well in the limit of low data and many variables
Bayesian Optimization
Design of Experiments
(Traditional)
Experiment #
Property
( is better)
0
50
Baird et al. Matter (2022)
Notes: , primarily because we are almost always in a very low data regime with high-dimensional search spaces. You'll get a funny look or a curt remark from a reviewer if you try to train a neural network on a few dozen points. These tend to overfit and have poor uncertainty quantification. Bayesian optimization, on the other hand, is incredibly good at quantifying uncertainty and balancing exploration of new designs with fine-tuning existing ones.

## Slide 8: A surrogate model predicts properties and quantifies uncertainty

## Slide 9: The acquisition function guides how to select the next experiment (in this case, neither the max predicted nor the max uncertainty)

## Slide 10: This Bayesian optimization loop continues iteratively (1) add data, (2) fit surrogate model (3) optimize acquisition function

## Slide 11: Real-world materials discovery tasks such as alloy design require more than “vanilla” optimization
High-dimensional
Compositional Linear Constraint
Mixed Continuous/Categorical
Multi-task
Multi-objective
NchooseK
nonlinear constraint

## Slide 12: Real-world materials discovery tasks such as alloy design require more than “vanilla” optimization
High-dimensional
Compositional Linear Constraint
Mixed Continuous/Categorical
Multi-task
Multi-objective
NchooseK
nonlinear constraint
Notes: Wave my magic wand to rearrange the text

## Slide 13: Real-world materials discovery tasks require more than “vanilla” optimization
Multi-task
Multi-objective
Mixed Continuous/Categorical
Compositional Linear Constraint
High-dimensional
NchooseK
nonlinear constraint
Single | Multi
Single | Multi
Continuous | Cont. + Categorical
No Constraint | Linear Constraint
Low dim. | High dim.
No Constraint | Nonlinear Constraint

## Slide 14: Real-world materials discovery tasks require more than “vanilla” optimization
Multi-task
Multi-objective
Mixed Continuous/Categorical
Compositional Linear Constraint
High-dimensional
NchooseK
nonlinear constraint
Single | Multi
Single | Multi
Continuous | Cont. + Categorical
No Constraint | Linear Constraint
Low dim. | High dim.
No Constraint | Nonlinear Constraint
Basic

## Slide 15: Real-world materials discovery tasks require more than “vanilla” optimization
Multi-task
Multi-objective
Mixed Continuous/Categorical
Compositional Linear Constraint
High-dimensional
NchooseK
nonlinear constraint
Single | Multi
Single | Multi
Continuous | Cont. + Categorical
No Constraint | Linear Constraint
Low dim. | High dim.
No Constraint | Nonlinear Constraint
Advanced

## Slide 16: Honegumi lets you quickly create advanced BO examples
Single obj. | Multi obj.
Single task | Multi task
Continuous | Cont. + Cat.
No Constraint | Linear
Low dim. | High dim.
No Constraint | Nonlinear
Single obj. | Multi obj.
Single task | Multi task
Continuous | Cont. + Cat.
No Constraint | Linear
Low dim. | High dim.
No Constraint | Nonlinear
Basic
Advanced
21 lines
62 lines
3x
Pairs well with LLMs

## Slide 17: Maximize the strength of a 3D printed part as a function of internal geometry and printer settings

## Slide 18: Honest caveat, in the same breath: as printed, these are tensegrity-inspired, not true tensegrity.
The black TPU members are not pre-tensioned — and they stretch.
Next: pre-tensioned prints, plus hand-built true-tensegrity validation specimens.
Printed PLA–TPU T3 prism, prc1kn — frame from our own 959 fps drop footage.
Notes: Say this the moment multi-material printing appears — do not let the audience discover it in Q&A. Pair it with the path forward (issue #87 pre-tensioning) so it reads as scope, not weakness.

## Slide 19: At 960 fps one frame is 1.04 ms — so the camera is not here for the impact.
Sony RX100 IV, 959 fps
It is here for the 150 ms after: rebound, sag, recovery
All of that lives below 100 Hz
Our own footage: prc1kn specimen, 60 in drop, 5-felt input (data/drop-tests/prc1kn-60in-5felt/video/).
Notes: Play it once, silently. Say the honest thing out loud: 960 fps cannot resolve a 1.6 ms pulse — one frame is 1.04 ms. The accelerometer owns the pulse; the camera owns everything after it, and everything after it is slow. Resolving specimen compression *during* the pulse would need >=5000 fps DIC (docs/drop-test-prc1kn-video-analysis.md, section 3).

## Slide 20: One clean shock, an elastic rebound, and the brake catches the carriage 79 ms later.
prc1kn drop 1, 959.04 fps — contact and turnaround are consecutive frames, 1.04 ms apart.
Notes: Walk it left to right in one sentence: entry, contact, turnaround, rebound, brake catch, hold. Do not claim the montage resolves the pulse — contact and turnaround are adjacent frames. What it does prove is rig physics and specimen integrity: one shock per drop, no plastic deformation, and the anti-rebound brake catching 150 mm above the stack.

## Slide 21: The camera brackets the pulse in one frame; the DAQ puts 190 samples inside it.
Camera: 1.04 ms per frame
DAQ: 8 µs per sample, 1.57 ms pulse
Camera still earns its keep: e* = 0.45 and a 79 ms brake catch
prc1kn drop 1, 959 fps — the entire deceleration is the single step at t = 0; the TP4 samples at 125 kHz.
Notes: This is the credibility slide, and it works by conceding the limit rather than hiding it. Point at the step: there are no camera samples inside the pulse, only on either side of it. That is why the accelerometer, not the video, produces the objectives. The camera's own deliverable is the scale-free coefficient of restitution (0.45) — a free reusability metric — plus rig physics and specimen integrity. Do not say the two instruments 'agree on the same drop': the prc1kn videos were shot ~5.5 h before that DAQ campaign, so drop-level pairing is not possible (docs/drop-test-prc1kn-video-analysis.md).

## Slide 22: A drop tower with an instrumented payload measures the force that actually reaches the payload.
Lansmont M23 tower · Dytran 3133A4 accelerometers
TP4 DAQ at 125 kHz — this is the instrument that sees the pulse
Standard test: 60 in drop onto 5 felts, repeated per specimen
Setup and standard conditions per the drop-test protocol (PR #86 branch); 25 kHz is the measured floor for the current pipeline (issue #89 sample-rate study).
Notes: Add a photo of the tower here before the talk if one is available; the text is a stand-in, not a design choice.

## Slide 23: SAE J211 filtering turns raw ringing into the three numbers the optimizer actually uses.
Peak transmitted force · specific energy absorbed · compaction efficiency
Raw vs. CFC-1000 vs. CFC-180 on the same impact window.
Notes: Do not explain the filter classes. Say: raw data ring at mounting resonance, the standard filter removes it, and what survives is the objective function.

## Slide 24: Our sensors lied to us first — cross-calibration caught a 5% error before it reached the optimizer.
A mis-entered sensitivity made channel 5 read 0.953× channel 4.
Channel 1 was clipping at the highest drops and we could not see it.
Fix: regress every channel against every other, every campaign.
Calibration story documented in PR #74.
Notes: This is the challenge slide Sterling asked to intersperse. It buys enormous credibility: we found our own error, and the cross-check is now routine.

## Slide 25: Working slide: challenges and where each one gets told
Sensor sensitivity error → cross-calibration → own slide (24)
Channel clipping at high drops → headroom check → spoken on slide 22
No camera resolves the 1.6 ms pulse → DAQ owns it → slide 21
Felt stack drifts with use → replace on schedule → spoken on slide 22
Print defects confound specimens → replicates → Q&A backup
Cables not in tension → pre-tensioned prints → slide 18
Notes: Planning aid. Delete before the talk.

## Slide 26: Working slide: media inventory and what still needs shooting
EMBEDDED HERE: Titan descent · 2D tensegrity · SUPERball drop · our 960 fps drop
ONLINE: print timelapses on YouTube — Insert ▸ Video ▸ Online Video; keep a local copy as backup
STILL NEEDED: drop-tower photo, printer bed shot, campaign ledger and Pareto-front figures
Notes: Planning aid. Delete before the talk.